# Capture (Actions)

The information is relevant for version 2.9.34 and later.

Description of Capture Actions.
## Set audio gain
Sets the level of audio gain for the output signal.
Parameters
Param1 - gain level. Possible values: 2.0 = +6 dB, 0.5 = -6 dB.
## Disable Action handler
Disables the Internal Actions handler. The function allows you to disable the mark detection in the input signal while broadcasting live.
Parameters
Param1 - name of the disabled handler.
## Enable Action handler
Enables the Internal Actions handler.
Parameters
Param1 - name of the enabled handler.
## Add Action handler
Registers a new handler for Internal Actions in the system.
Parameters
- Param1 - handler type:
  - dtmf
  - vbi
  - vdetect
  - stilldetect
  - alevel
- Param2 - new handler name.
- Param3 - string with the “code” settings for the selected handler type. The string format is described in the module´s help information. To display help, run ecapture.exe –help.
- Param4 - string with the “channel” settings for the selected handler type. The string format is described in the module´s help information. To display help, run ecapture.exe –help.
- Param5 - target URL in the host:port format.
## Delete Action Handler
Deletes the Internal Actions handler.
Parameters
Param1 - name of the deleted handler.
## Reload
Sends the command to reload the module. Used when the selected module needs reloading without stopping the broadcast to restart the whole server.
Parameters
No parameters.
## Reconnect Hardware
Sends the command to reconnect to the I/O board. Used when there’s a problem with the driver stability for long periods of time or after the input signal has been restored.
Parameters
No parameters.
## Set Source
Sets the input stream for Capture in the IP mode.
Parameters
- Param1 - string with the stream data for:
  - WebCast - url in a usual format
  - IPTS - “ip_addr:port[@pgm=N][@vpid=N][@apid=N]..[@apid=N]”
  - NDI - “COM+ (STREAM)”.
## Set Channel Map
New settings for Audio Channel Map.
Parameters
- Param1
  - configuration string in the C#/C#/C# format
  - empty string resets settings to the default value.